## Slide 1: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 1: Introduction

## Slide 2
Text Book:
T1. Patterson, D.A. & J.L. Hennessy. Computer Organization and Design: The Hardware/Software Interface. Elsevier, 6th edition., 2021.
Reference Books:
(i) Hamacher et. al. Computer Organization, McGraw Hill, 5th ed., 2002.
(ii) J.L. Hennessy & D.A. Patterson. Computer Architecture: A Quantitative Approach. Morgan Kauffmann, 5th Ed, 2012.
(iii)W. Stallings. Computer Organization & Architecture. PHI, 6th ed., 2004.
Text Books

## Slide 3
Lecture hours
  Monday, Wednesday, and Friday: 9.00am – 9.50am.
  Please switch off (or put in silent mode) your mobile phones while you are in the class
Contact Hours
  Wednesday (10.00pm to 11.00pm)
Course material: CMS (Lect ppt)
Quiz: (tentative): 4th week of Oct 2022, 4th week of Nov 2022
Lab Quizzes (tentative): 4th week of Oct 2022, 4th week of Nov 2022
Mid-Sem: Duration (1.5 Hrs.), Weightage (30%), Date: 31/10/2022
Comprehensive: Duration (3 Hrs.), Weightage (40%), Date: 19/12/2022
Course Administration

## Slide 4
Because you use it everyday,
Because you will likely use it for the rest of your life,
Because you are a CS major, studying computer science.
Because computer architecture is perhaps the most fundamental subject in computer science. Without computers, the field of computer science does not exist.
The subject explores how machines are designed, built, and operate.
Computer architectures represent the means of interconnectivity for a computer's hardware components as well as the mode of data transfer and processing exhibited.
Why Study Computer Architecture?

## Slide 5
The first step in understanding any computer architecture is to learn its language. The words in a computer’s language are called instructions.
The computer’s vocabulary is called the instruction set.
All programs running on a computer use the same instruction set.
Even complex software applications, such as word processing and spreadsheet applications, are eventually compiled into a series of simple instructions such as add, subtract, and branch.
Computer instructions indicate both the operation to perform and the operands to use. The operands may come from memory, from registers, or from the instruction itself.
Computer Architecture

## Slide 6
Progress in computer technology
  Underpinned by domain-specific accelerators
Makes novel applications feasible
  Computers in automobiles
  Cell phones
  Human genome project
  World Wide Web
  Search Engines
Computers are pervasive
The Computer Revolution

## Slide 7
Personal computers
  General purpose, variety of software
  Subject to cost/performance tradeoff
Server computers
  Network based
  High capacity, performance, reliability
  Range from small servers to building sized
Classes of Computers

## Slide 8
Supercomputers
  Type of server
  High-end scientific and engineering calculations
  Highest capability but represent a small fraction of the overall computer market
Embedded computers
  Hidden as components of systems
  Stringent power/performance/cost constraints
Classes of Computers

## Slide 9
The PostPC Era

## Slide 10
Personal Mobile Device (PMD)
  Battery operated
  Connects to the Internet
  Hundreds of dollars
  Smart phones, tablets, electronic glasses
Cloud computing
  Warehouse Scale Computers (WSC)
  Software as a Service (SaaS)
  Portion of software run on a PMD and a portion run in the Cloud
  Amazon and Google
The PostPC Era

## Slide 11
How programs are translated into the machine language
  And how the hardware executes them
The hardware/software interface
What determines program performance
  And how it can be improved
How hardware designers improve performance
What is parallel processing
What You Will Learn

## Slide 12
Algorithm
  Determines number of operations executed
Programming language, compiler, architecture
  Determine number of machine instructions executed per operation
Processor and memory system
  Determine how fast instructions are executed
I/O system (including OS)
  Determines how fast I/O operations are executed
Understanding Performance

## Slide 13
Use abstraction to simplify design
Make the common case fast
Performance via parallelism
Performance via pipelining
Performance via prediction
Hierarchy of memories
Dependability via redundancy
Seven Great Ideas

## Slide 14
Below Your Program
Application software
  Written in high-level language
System software
  Compiler: translates HLL code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers

## Slide 15
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data
Levels of Program Code

## Slide 16
Opening the Box

## Slide 17
Datapath: performs operations on data
Control: sequences datapath, memory, ...
Cache memory
  Small fast SRAM memory for immediate access to data
Inside the Processor (CPU)

## Slide 18
A12 processor
Inside the Processor

## Slide 19
Abstractions
The BIG Picture
Abstraction helps us deal with complexity
  Hide lower-level detail
Instruction set architecture (ISA)
  The hardware/software interface
Application binary interface
  The ISA plus system software interface
Implementation
  The details underlying and interface

## Slide 20
Electronics technology continues to evolve
  Increased capacity and performance
  Reduced cost
Technology Trends
DRAM capacity
Year | Technology | Relative performance/cost | 
1951 | Vacuum tube | 1 | 
1965 | Transistor | 35 | 
1975 | Integrated circuit (IC) | 900 | 
1995 | Very large scale IC (VLSI) | 2,400,000 | 
2013 | Ultra large scale IC | 250,000,000,000 | 

## Slide 21
Intel® Core 10th Gen
300mm wafer, 506 chips, 10nm technology
Each chip is 11.4 x 10.7 mm
Yield: proportion of working dies per wafer (built from silicon ingot)

## Slide 22
Integrated Circuit Cost
Nonlinear relation to area and defect rate
  Wafer cost and area are fixed
  Defect rate determined by manufacturing process
  Die area determined by architecture and circuit design

## Slide 23
Defining Performance
Which airplane has the best performance?

## Slide 24
Response Time and Throughput
Response time
  How long it takes to do a task
Throughput
  Total work done per unit time
    e.g., tasks/transactions/… per hour
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
We’ll focus on response time for now…

## Slide 25
Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B

## Slide 26
Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
  Different programs are affected differently by CPU and system performance

## Slide 27
CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz

## Slide 28
CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count

## Slide 29
CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?

## Slide 30
Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction (CPI)
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 31
CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?

## Slide 32
CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency

## Slide 33
CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 34
Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, clock rate(Tc
The BIG Picture

## Slide 35
Power Trends
In CMOS IC technology
×1000
×30
5V → 1V

## Slide 36
Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 37
Uniprocessor Performance
Constrained by power, instruction-level parallelism, memory latency

## Slide 38
Multiprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization

## Slide 39
SPEC CPU Benchmark
Programs used to measure performance
  Supposedly typical of actual workload
Standard Performance Evaluation Corp (SPEC)
  Develops benchmarks for CPU, I/O, Web, …
SPEC CPU2006
  Elapsed time to execute a selection of programs
    Negligible I/O, so focuses on CPU performance
  Normalize relative to reference machine
  Summarize as geometric mean of performance ratios
    CINT2006 (integer) and CFP2006 (floating-point)

## Slide 40
SPEC Power Benchmark
Power consumption of server at different workload levels
  Performance: ssj_ops/sec
  Power: Watts (Joules/sec)

## Slide 41
THANK YOU

## Slide 42: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 2: Introduction

## Slide 43
Defining Performance
Which airplane has the best performance?

## Slide 44
Response Time and Throughput
Response time
  How long it takes to do a task
Throughput
  Total work done per unit time
    e.g., tasks/transactions/… per hour
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
We’ll focus on response time for now…

## Slide 45
Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B

## Slide 46
Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
  Different programs are affected differently by CPU and system performance

## Slide 47
CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz

## Slide 48
Clock cycle/Clock cycle time: The time period of the processor clock that forms the basis for the components within a processor to synchronize in order to perform their activity.
Clock Rate: The number of cycles the processor clock generates per second.
Instruction/Instruction set: Code that allows the processor to understand the operation that is intended to perform. Every processor has a set of instructions which enable only those operations defined by such instructions and is known as instruction set of a processor.
Execution time/cpu time: the time taken for a processor to complete the execution of a program completely.
Cycles per instruction: This parameter indicates the average number of cycles consumed by an instruction for its execution.
Definitions

## Slide 49
CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count
For a program,

## Slide 50
CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?

## Slide 51
Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction (CPI)
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 52
CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?

## Slide 53
CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 54: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 3: Performance, MIPS Instrutcion

## Slide 55
CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency

## Slide 56
Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, clock rate(Tc
The BIG Picture

## Slide 57
Uniprocessor Performance
Constrained by power, instruction-level parallelism, memory latency

## Slide 58
Multicore microprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization

## Slide 59
SPEC CPU Benchmark
Programs used to measure performance
  Supposedly typical of actual workload
Standard Performance Evaluation Corp (SPEC)
  Develops benchmarks for CPU, I/O, Web, …
SPEC CPU2017
  Elapsed time to execute a selection of programs
    Negligible I/O, so focuses on CPU performance
  Set of 10 integer benchmarks and 13 floating point benchmarks
  Summarize as geometric mean of performance ratios

## Slide 60
SPEC Power Benchmark
Power consumption of server at different workload levels
  Performance: ssj_ops/sec
  Power: Watts (Joules/sec)

## Slide 61
Pitfall: Amdahl’s Law
Improving an aspect of a computer and expecting a proportional improvement in overall performance
  Can’t be done!
Example: multiply accounts for 80s/100s
  How much improvement in multiply performance to get 5× overall?

## Slide 62
In computer architecture, Amdahl’s law (or Amdahl’s Argument) is a formula which gives the theoretical speedup in latency of the execution of a task at fixed workload that can be expected of a system whose resources are improved. It is named after the computer scientist Gene Amdahl.
The speedup formula is given by ,
speedup = Execution time without enhancement = Execution Timeold
Execution Time with enhancement Execution Timenew
Execution Timenew = Execution Timeold x ((1- Fraction enhanced) + (FractionEnhanced / SpeedupEnhanced ))
overall speedup = 1/ ((1- Fraction enhanced) + (FractionEnhanced / SpeedupEnhanced ))
Amdahl’s law

## Slide 63
a) Given , Speedupenhanced = 20
Fraction enhanced =0.5
overall speedup =?
overall speedup = 1/((1-0.5) + 0.5/20) = 1.105
b) Given , Speedupenhanced =16
Fraction enhanced = 0.6
overall speedup = ?
overall speedup = 1/((1-0.6) + 0.6/16) = 2.286.
Example

## Slide 65
Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets

## Slide 66
The MIPS Instruction Set
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Typical of many modern ISAs
  See MIPS Reference Data tear-out card, and Appendixes B and E
Similar ISAs have a large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …

## Slide 67
Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favors regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost

## Slide 68
Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1

## Slide 69
Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations

## Slide 70
Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1

## Slide 71
Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4
MIPS is Big Endian
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address

## Slide 72
Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0

## Slide 73
Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word

## Slide 74: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 4: MIPS

## Slide 75
Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0

## Slide 76
Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word

## Slide 77
Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 78
Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
  addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction

## Slide 79
The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add $t2, $s1, $zero

## Slide 80
Representing Instructions
Instructions are encoded in binary
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
Register numbers
  $t0 – $t7 are reg’s 8 – 15
  $t8 – $t9 are reg’s 24 – 25
  $s0 – $s7 are reg’s 16 – 23

## Slide 81
MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 82
R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 83
MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 84: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 5: MIPS Instructions

## Slide 85
R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 86
MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 89
Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Shift left | << | << | sll
Shift right | >> | >>> | srl
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise NOT | ~ | ~ | nor
Useful for extracting and inserting groups of bits in a word

## Slide 90
Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 91
AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 92
OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0

## Slide 93
NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero

## Slide 94
Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1

## Slide 95
Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in $s0, $s1, …
Compiled MIPS code:
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: …

## Slide 96
Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 j Loop Exit: …

## Slide 97: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 6: MIPS Instructions contd…

## Slide 98
MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 101
Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture

## Slide 102
Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Shift left | << | << | sll
Shift right | >> | >>> | srl
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise NOT | ~ | ~ | nor
Useful for extracting and inserting groups of bits in a word

## Slide 103
Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 104
AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 105
OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0

## Slide 106
NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero

## Slide 107
Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1

## Slide 108
Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in $s0, $s1, …
Compiled MIPS code:
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: …

## Slide 109
Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 j Loop Exit: …

## Slide 110
More Conditional Operations
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L

## Slide 111
Branch Instruction Design
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  Combining with branch involves more work per instruction, requiring a slower clock
  All instructions penalized!
beq and bne are the common case
This is a good design compromise

## Slide 112
Signed vs. Unsigned
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0

## Slide 113
Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization
An advanced processor can accelerate execution of basic blocks

## Slide 114
Unsigned Binary Integers
Chapter 2 — Instructions: Language of the Computer — 114
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295

## Slide 115
2s-Complement Signed Integers
Given an n-bit number
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 1111 1111 1111 1111 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
Using 32 bits
  –2,147,483,648 to +2,147,483,647

## Slide 116
2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 117
Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 00102
  –2 = 1111 1111 … 11012 + 1 = 1111 1111 … 11102

## Slide 118
Sign Extension
Representing a number using more bits
  Preserve the numeric value
In MIPS instruction set
  addi: extend immediate value
  lb, lh: extend loaded byte/halfword
  beq, bne: extend the displacement
Replicate the sign bit to the left
  unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110

## Slide 119
Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 120
Procedure Calling
Steps required
  Place parameters in registers
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call

## Slide 121
Register Usage
$a0 – $a3: arguments (reg’s 4 – 7)
$v0, $v1: result values (reg’s 2 and 3)
$t0 – $t9: temporaries
  Can be overwritten by callee
$s0 – $s7: saved
  Must be saved/restored by callee
$gp: global pointer for static data (reg 28)
$sp: stack pointer (reg 29)
$fp: frame pointer (reg 30)
$ra: return address (reg 31)

## Slide 122
Procedure Call Instructions
Procedure call: jump and link
jal ProcedureLabel
  Address of following instruction put in $ra
  Jumps to target address
Procedure return: jump register
jr $ra
  Copies $ra to program counter
  Can also be used for computed jumps
    e.g., for case/switch statements

## Slide 123
Leaf Procedure Example
C code:
int leaf_example (int g, h, i, j) { int f; f = (g + h) - (i + j); return f; }
  Arguments g, …, j in $a0, …, $a3
  f in $s0 (hence, need to save $s0 on stack)
  Result in $v0

## Slide 124
Leaf Procedure Example
MIPS code:
leaf_example: addi $sp, $sp, -4 sw $s0, 0($sp) add $t0, $a0, $a1 add $t1, $a2, $a3 sub $s0, $t0, $t1 add $v0, $s0, $zero lw $s0, 0($sp) addi $sp, $sp, 4 jr $ra

## Slide 125: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 7: Non-leaf Procedure MIPS

## Slide 126
Non-Leaf Procedures
Procedures that call other procedures
For nested call, caller needs to save on the stack:
  Its return address
  Any arguments and temporaries needed after the call
Restore from the stack after the call

## Slide 127
Non-Leaf Procedure Example
C code:
int fact (int n) { if (n < 1) return f; else return n * fact(n - 1); }
  Argument n in $a0
  Result in $v0

## Slide 128
Non-Leaf Procedure Example
MIPS code:
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # save argument slti $t0, $a0, 1 # test for n < 1 beq $t0, $zero, L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # else decrement n jal fact # recursive call lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return

## Slide 129: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 8: MIPS Branching

## Slide 130
Local Data on the Stack
Local data allocated by callee
  e.g., C automatic variables
Procedure frame (activation record)
  Used by some compilers to manage stack storage

## Slide 131
Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
  $gp initialized to address allowing ±offsets into this segment
Dynamic data: heap
  E.g., malloc in C, new in Java
Stack: automatic storage

## Slide 132
Character Data
Byte-encoded character sets
  ASCII: 128 characters
    95 graphic, 33 control
  Latin-1: 256 characters
    ASCII, +96 more graphic characters
Unicode: 32-bit character set
  Used in Java, C++ wide characters, …
  Most of the world’s alphabets, plus symbols
  UTF-8, UTF-16: variable-length encodings

## Slide 133
Byte/Halfword Operations
Could use bitwise operations
MIPS byte/halfword load/store
  String processing is a common case
lb rt, offset(rs) lh rt, offset(rs)
  Sign extend to 32 bits in rt
lbu rt, offset(rs) lhu rt, offset(rs)
  Zero extend to 32 bits in rt
sb rt, offset(rs) sh rt, offset(rs)
  Store just rightmost byte/halfword

## Slide 134
String Copy Example
C code (naïve):
  Null-terminated string
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
  Addresses of x, y in $a0, $a1
  i in $s0

## Slide 135
String Copy Example
MIPS code:
strcpy: addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $zero, $zero # i = 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 = y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] = y[i] beq $t2, $zero, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i = i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return

## Slide 136
32-bit Constants
0000 0000 0111 1101 0000 0000 0000 0000
Most constants are small
  16-bit immediate is sufficient
For the occasional 32-bit constant
lui rt, constant
  Copies 16-bit constant to left 16 bits of rt
  Clears right 16 bits of rt to 0
lhi $s0, 61
0000 0000 0111 1101 0000 1001 0000 0000
ori $s0, $s0, 2304

## Slide 137
Branch Addressing
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Forward or backward
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
PC-relative addressing
  Target address = PC + offset × 4
  PC already incremented by 4 by this time

## Slide 138
Jump Addressing
Jump (j and jal) targets could be anywhere in text segment
  Encode full address in instruction
op
address
6 bits
26 bits
(Pseudo)Direct jump addressing
  Target address = PC31…28 : (address × 4)

## Slide 139
Target Addressing Example
Loop code from earlier example
  Assume Loop at location 80000
Loop: sll $t1, $s3, 2 | 80000 | 0 | 0 | 19 | 9 | 4 | 0
add $t1, $t1, $s6 | 80004 | 0 | 9 | 22 | 9 | 0 | 32
lw $t0, 0($t1) | 80008 | 35 | 9 | 8 | 0 |  | 
bne $t0, $s5, Exit | 80012 | 5 | 8 | 21 | 2 |  | 
addi $s3, $s3, 1 | 80016 | 8 | 19 | 19 | 1 |  | 
j Loop | 80020 | 2 | 20000 |  |  |  | 
Exit: … | 80024 |  |  |  |  |  | 

## Slide 140
Branching Far Away
If branch target is too far to encode with 16-bit offset, assembler rewrites the code
Example
  beq $s0,$s1, L1
  ↓
  bne $s0,$s1, L2 j L1 L2: …

## Slide 142
Addressing Mode Summary

## Slide 143
C Sort Example
Illustrates use of assembly instructions for a C bubble sort function
Swap procedure (leaf)
  void swap(int v[], int k) { int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
  v in $a0, k in $a1, temp in $t0

## Slide 144
The Procedure Swap
swap: sll $t1, $a1, 2 # $t1 = k * 4
add $t1, $a0, $t1 # $t1 = v+(k*4)
# (address of v[k])
lw $t0, 0($t1) # $t0 (temp) = v[k]
lw $t2, 4($t1) # $t2 = v[k+1]
sw $t2, 0($t1) # v[k] = $t2 (v[k+1])
sw $t0, 4($t1) # v[k+1] = $t0 (temp)
jr $ra # return to calling routine

## Slide 145
The Sort Procedure in C
Non-leaf (calls swap)
  void sort (int v[], int n)
  {
  int i, j;
  for (i = 0; i < n; i += 1) {
  for (j = i – 1;
  j >= 0 && v[j] > v[j + 1];
  j -= 1) {
  swap(v,j);
  }
  }
  }
  v in $a0, k in $a1, i in $s0, j in $s1

## Slide 146
The Procedure Body
move $s2, $a0 # save $a0 into $s2
move $s3, $a1 # save $a1 into $s3
move $s0, $zero # i = 0
for1tst: slt $t0, $s0, $s3 # $t0 = 0 if $s0 ≥ $s3 (i ≥ n)
beq $t0, $zero, exit1 # go to exit1 if $s0 ≥ $s3 (i ≥ n)
addi $s1, $s0, –1 # j = i – 1
for2tst: slti $t0, $s1, 0 # $t0 = 1 if $s1 < 0 (j < 0)
bne $t0, $zero, exit2 # go to exit2 if $s1 < 0 (j < 0)
sll $t1, $s1, 2 # $t1 = j * 4
add $t2, $s2, $t1 # $t2 = v + (j * 4)
lw $t3, 0($t2) # $t3 = v[j]
lw $t4, 4($t2) # $t4 = v[j + 1]
slt $t0, $t4, $t3 # $t0 = 0 if $t4 ≥ $t3
beq $t0, $zero, exit2 # go to exit2 if $t4 ≥ $t3
move $a0, $s2 # 1st param of swap is v (old $a0)
move $a1, $s1 # 2nd param of swap is j
jal swap # call swap procedure
addi $s1, $s1, –1 # j –= 1
j for2tst # jump to test of inner loop
exit2: addi $s0, $s0, 1 # i += 1
j for1tst # jump to test of outer loop

## Slide 147
The Full Procedure
sort: addi $sp,$sp, –20 # make room on stack for 5 registers
sw $ra, 16($sp) # save $ra on stack
sw $s3,12($sp) # save $s3 on stack
sw $s2, 8($sp) # save $s2 on stack
sw $s1, 4($sp) # save $s1 on stack
sw $s0, 0($sp) # save $s0 on stack
… # procedure body
…
exit1: lw $s0, 0($sp) # restore $s0 from stack
lw $s1, 4($sp) # restore $s1 from stack
lw $s2, 8($sp) # restore $s2 from stack
lw $s3,12($sp) # restore $s3 from stack
lw $ra,16($sp) # restore $ra from stack
addi $sp,$sp, 20 # restore stack pointer
jr $ra # return to calling routine

## Slide 148
Arrays vs. Pointers
Array indexing involves
  Multiplying index by element size
  Adding to array base address
Pointers correspond directly to memory addresses
  Can avoid indexing complexity

## Slide 149
Example: Clearing and Array
clear1(int array[], int size) { int i; for (i = 0; i < size; i += 1) array[i] = 0; } | clear2(int *array, int size) { int *p; for (p = &array[0]; p < &array[size]; p = p + 1) *p = 0; }
move $t0,$zero # i = 0 loop1: sll $t1,$t0,2 # $t1 = i * 4 add $t2,$a0,$t1 # $t2 = # &array[i] sw $zero, 0($t2) # array[i] = 0 addi $t0,$t0,1 # i = i + 1 slt $t3,$t0,$a1 # $t3 = # (i < size) bne $t3,$zero,loop1 # if (…) # goto loop1 | move $t0,$a0 # p = & array[0] sll $t1,$a1,2 # $t1 = size * 4 add $t2,$a0,$t1 # $t2 = # &array[size] loop2: sw $zero,0($t0) # Memory[p] = 0 addi $t0,$t0,4 # p = p + 4 slt $t3,$t0,$t2 # $t3 = #(p<&array[size]) bne $t3,$zero,loop2 # if (…) # goto loop2

## Slide 151
Additional exercise problems (Tuts)

## Slide 152
Question 1) You have a system that contains a special processor for doing floating-point operations. You have determined that 50% of your computations can use the floating-point processor . The speedup of the floating point processor is 8.
a)Compute the overall speedup achieved by using the floating-point processor.
b)Compute the overall speedup achieved if you modify the compiler so that 62% of the
computations can use the floating-point processor.
Question 2) What is the speedup that could be achieved according to Amdahl’s Law if infinite number of processors are utilized for optimizing the program execution, given the fact that 5% of a program is sequential and the remaining part is ideally parallel?

## Slide 153: Question-4
Q4. Convert the following C statements to equivalent MIPS assembly language. Assume that the variables f, g, h are assigned to registers $s0, $s1, $s2 respectively.
Assume that the base address of the array A and B are in registers $s6 and $s7 respectively.
a) f = g + h + B[4]
b) f = h + A[B[4]]

## Slide 154: Question-5
Q5. If the instruction set of the MIPS processor is modified, the instruction format must also be changed. For each of the suggested changes, show the size of the bit fields of an R-type format instruction. What is the total number of bits needed for each instruction?
8 registers.
10 bit immediate constants
128 Registers.

## Slide 155: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 10: Arithmetic for Computers

## Slide 156
Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
Floating-point real numbers
  Representation and operations

## Slide 157
Integer Addition
Example: 7 + 6
Overflow if result out of range
  Adding +ve and –ve operands, no overflow
  Adding two +ve operands
    Overflow if result sign is 1
  Adding two –ve operands
    Overflow if result sign is 0

## Slide 158
Integer Subtraction
Add negation of second operand
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Overflow if result out of range
  Subtracting two +ve or two –ve operands, no overflow
  Subtracting +ve from –ve operand
    Overflow if result sign is 0
  Subtracting –ve from +ve operand
    Overflow if result sign is 1

## Slide 159
Dealing with Overflow
Some languages (e.g., C) ignore overflow
  Use MIPS addu, addui, subu instructions
Other languages (e.g., Ada, Fortran) require raising an exception
  Use MIPS add, addi, sub instructions
  On overflow, invoke exception handler
    Save PC in exception program counter (EPC) register
    Jump to predefined handler address
    mfc0 (move from coprocessor reg) instruction can retrieve EPC value, to return after corrective action

## Slide 160
Multiplication
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product

## Slide 161
Multiplication Hardware
Initially 0

## Slide 162
Optimized Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low

## Slide 163
Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel

## Slide 164: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 11: Multiplication/Divisor Hardware

## Slide 165
Multiplication
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product

## Slide 166
Multiplication Hardware
Initially 0

## Slide 167
Optimized Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low
Multiplier is in the right half of product reg

## Slide 168
Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel

## Slide 169
MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product –> rd

## Slide 170
Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor

## Slide 171
Division Hardware
Initially dividend at right
Initially divisor in left half

## Slide 172
Faster Division
Can’t use parallel hardware as in multiplier
  Subtraction is conditional on sign of remainder
Faster dividers (e.g. SRT division) generate multiple quotient bits per step
  Still require multiple steps

## Slide 173
MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder
  LO: 32-bit quotient
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking
    Software must perform checks if required
  Use mfhi, mflo to access result

## Slide 174: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 12: Floating Points

## Slide 175
Floating Point
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy

## Slide 176
Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 177
IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 178
In IEEE 754 floating point numbers, the exponent is biased in the engineering sense of the word – the value stored is offset from the actual value by the exponent bias.
Biasing is done because exponents have to be signed values in order to be able to represent both tiny and huge values, but two's complement, the usual representation for signed values, would make comparison harder.
To solve this problem the exponent is biased before being stored, by adjusting its value to put it within an unsigned range suitable for comparison.
By arranging the fields so that the sign bit is in the most significant bit position, the biased exponent in the middle, then the mantissa in the least significant bits, the resulting value will be ordered properly, whether it's interpreted as a floating point or integer value. This allows high speed comparisons of floating point numbers using fixed point hardware.
When interpreting the floating-point number, the bias is subtracted to retrieve the actual exponent.
For a single-precision number, an exponent in the range −126 .. +127 is biased by adding 127 to get a value in the range 1 .. 254 (0 and 255 have special meanings). For a double-precision number, an exponent in the range −1022 .. +1023 is biased by adding 1023 to get a value in the range 1 .. 2046 (0 and 2047 have special meanings).
More on bias

## Slide 179
Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  exponent: 11111110  actual exponent = 254 – 127 = +127

## Slide 180
Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023

## Slide 181
Floating-Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 182
Floating-Point Example
What number is represented by the single-precision float
11000000101000…00
  S = 1
  Fraction = 01000…002
  xponent = 100000012 = 129
x = (–1)1 × (1 + 012) × 2(129 – 127)
  = (–1) × 1.25 × 22
  = –5.0

## Slide 183
Floating-Point Addition
Consider a 4-digit decimal example
  9.999 × 101 + 1.610 × 10–1
1. Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102

## Slide 184
Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625

## Slide 185
FP Adder Hardware
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined

## Slide 186
FP Adder Hardware
Step 1
Step 2
Step 3
Step 4

## Slide 187
FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP  integer conversion
Operations usually takes several cycles
  Can be pipelined

## Slide 188
FP Instructions in MIPS
FP hardware is coprocessor 1
  Adjunct processor that extends the ISA
Separate FP registers
  32 single-precision: $f0, $f1, … $f31
  Paired for double-precision: $f0/$f1, $f2/$f3, …
    Release 2 of MIPs ISA supports 32 × 64-bit FP reg’s
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  lwc1, ldc1, swc1, sdc1
    e.g., ldc1 $f8, 32($sp)

## Slide 189
FP Instructions in MIPS
Single-precision arithmetic
  add.s, sub.s, mul.s, div.s
    e.g., add.s $f0, $f1, $f6
Double-precision arithmetic
  add.d, sub.d, mul.d, div.d
    e.g., mul.d $f4, $f4, $f6
Single- and double-precision comparison
  c.xx.s, c.xx.d (xx is eq, lt, le, …)
  Sets or clears FP condition-code bit
    e.g. c.lt.s $f3, $f4
Branch on FP condition code true or false
  bc1t, bc1f
    e.g., bc1t TargetLabel

## Slide 190
FP Example: Array Multiplication
X = X + Y × Z
  All 32 × 32 matrices, 64-bit double-precision elements
C code:
void mm (double x[][], double y[][], double z[][]) { int i, j, k; for (i = 0; i! = 32; i = i + 1) for (j = 0; j! = 32; j = j + 1) for (k = 0; k! = 32; k = k + 1) x[i][j] = x[i][j] + y[i][k] * z[k][j]; }
  Addresses of x, y, z in $a0, $a1, $a2, and i, j, k in $s0, $s1, $s2

## Slide 191
FP Example: Array Multiplication
MIPS code:
li $t1, 32 # $t1 = 32 (row size/loop end) li $s0, 0 # i = 0; initialize 1st for loop L1: li $s1, 0 # j = 0; restart 2nd for loop L2: li $s2, 0 # k = 0; restart 3rd for loop sll $t2, $s0, 5 # $t2 = i * 32 (size of row of x) addu $t2, $t2, $s1 # $t2 = i * size(row) + j sll $t2, $t2, 3 # $t2 = byte offset of [i][j] addu $t2, $a0, $t2 # $t2 = byte address of x[i][j] l.d $f4, 0($t2) # $f4 = 8 bytes of x[i][j] L3: sll $t0, $s2, 5 # $t0 = k * 32 (size of row of z) addu $t0, $t0, $s1 # $t0 = k * size(row) + j sll $t0, $t0, 3 # $t0 = byte offset of [k][j] addu $t0, $a2, $t0 # $t0 = byte address of z[k][j] l.d $f16, 0($t0) # $f16 = 8 bytes of z[k][j] …

## Slide 192
FP Example: Array Multiplication
… sll $t0, $s0, 5 # $t0 = i*32 (size of row of y) addu $t0, $t0, $s2 # $t0 = i*size(row) + k sll $t0, $t0, 3 # $t0 = byte offset of [i][k] addu $t0, $a1, $t0 # $t0 = byte address of y[i][k] l.d $f18, 0($t0) # $f18 = 8 bytes of y[i][k] mul.d $f16, $f18, $f16 # $f16 = y[i][k] * z[k][j] add.d $f4, $f4, $f16 # f4=x[i][j] + y[i][k]*z[k][j] addiu $s2, $s2, 1 # $k k + 1 bne $s2, $t1, L3 # if (k != 32) go to L3 s.d $f4, 0($t2) # x[i][j] = $f4 addiu $s1, $s1, 1 # $j = j + 1 bne $s1, $t1, L2 # if (j != 32) go to L2 addiu $s0, $s0, 1 # $i = i + 1 bne $s0, $t1, L1 # if (i != 32) go to L1

## Slide 193: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 13: The Processor

## Slide 194
Introduction
CPU performance factors
  Instruction count
    Determined by ISA and compiler
  CPI and Cycle time
    Determined by CPU hardware
We will examine two MIPS implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: lw, sw
  Arithmetic/logical: add, sub, and, or, slt
  Control transfer: beq, j

## Slide 195
Instruction Execution
PC  instruction memory, fetch instruction
Register numbers  register file, read registers
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch target address
  Access data memory for load/store
  PC  target address or PC + 4

## Slide 196
CPU Overview

## Slide 197
Multiplexers
Can’t just join wires together
  Use multiplexers

## Slide 198
Control

## Slide 199
Logic Design Basics
Information encoded in binary
Low voltage = 0, High voltage = 1
One wire per bit
Multi-bit data encoded on multi-wire buses
Combinational element
Operate on data
Output is a function of input
State (sequential) elements
Store information

## Slide 200
Combinational Elements
AND-gate
  Y = A & B
A
B
Y
I0
I1
Y
M u x
S
Multiplexer
  Y = S ? I1 : I0
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)

## Slide 201
Sequential Elements
Register: stores data in a circuit
  Uses a clock signal to determine when to update the stored value
  Edge-triggered: update when Clk changes from 0 to 1
D
Clk
Q
Clk
D
Q

## Slide 202
Sequential Elements
Register with write control
  Only updates on clock edge when write control input is 1
  Used when stored value is required later
D
Clk
Q
Write
Write
D
Q
Clk

## Slide 203
Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element
  Longest delay determines clock period

## Slide 204
Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a MIPS datapath incrementally
  Refining the overview design

## Slide 205
Instruction Fetch
32-bit register
Increment by 4 for next instruction

## Slide 206
R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 207: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 14: The Processor: Full datapath

## Slide 208
Instruction Fetch
32-bit register
Increment by 4 for next instruction

## Slide 209
R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 210
Load/Store Instructions
Read register operands
Calculate address using 16-bit offset
Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory

## Slide 211
Branch Instructions
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to PC + 4
    Already calculated by instruction fetch

## Slide 212
Branch Instructions
Just re-routes wires
Sign-bit wire replicated

## Slide 213
Composing the Elements
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 214
R-Type/Load/Store Datapath

## Slide 215
Full Datapath

## Slide 216
ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on funct field
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 217
ALU Control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw | 00 | load word | XXXXXX | add | 0010
sw | 00 | store word | XXXXXX | add | 0010
beq | 01 | branch equal | XXXXXX | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control

## Slide 218
The Main Control Unit
Control signals derived from instruction
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
Branch
opcode
always read
read, except for load
write for R-type and load
sign-extend and add

## Slide 219
Datapath With Control

## Slide 220
MIPS Control Signal Summary

## Slide 221: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 15: The Processor: Datapath with Jumps

## Slide 222
R-Type Instruction

## Slide 223
Load Instruction

## Slide 224
Branch-on-Equal Instruction

## Slide 225
Implementing Jumps
Jump uses word address
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
  00
Need an extra control signal decoded from opcode
2
address
31:26
25:0
Jump

## Slide 226
Datapath With Jumps Added

## Slide 227
Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 228: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 16: Pipelining

## Slide 229
Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance

## Slide 230
MIPS Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 231
Basic MIPS (RISC) Pipelining

## Slide 232
Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 233
Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 234: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 17: Pipelining and Hazards

## Slide 235
Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = (Time between instructionsnonpipelined)/(Number of stages)
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease

## Slide 236
Pipelining and ISA Design
MIPS ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage
  Alignment of memory operands
    Memory access takes only one cycle

## Slide 237
Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 238: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 18: Pipeline Registers

## Slide 239
Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 240
Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation

## Slide 241
Pipeline registers
Need registers between stages
  To hold information produced in previous cycle

## Slide 242
IF for Load, Store, …

## Slide 243
ID for Load, Store, …

## Slide 244
EX for Load

## Slide 245
MEM for Load

## Slide 246
WB for Load
Wrong register number

## Slide 247
Corrected Datapath for Load

## Slide 248
EX for Store

## Slide 249
MEM for Store

## Slide 250
WB for Store

## Slide 251
Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 252
Multi-Cycle Pipeline Diagram
Traditional form

## Slide 253
Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 254
Addressing Structural Hazard
Duplicate Resources
Pipeline Resources
Reorder Resources
Stall the pipeline, if above methods are costly

## Slide 255: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 19: Data Hazard

## Slide 256
Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3

## Slide 257
Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 258
Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!

## Slide 259
Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles

## Slide 260
Data Hazards in ALU Instructions
Consider this sequence:
  sub $2, $1,$3 and $12,$2,$5 or $13,$6,$2 add $14,$2,$2 sw $15,100($2)
We can resolve hazards with forwarding
  How do we detect when to forward?

## Slide 261
Dependencies & Forwarding

## Slide 262
Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs = register number for Rs sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs, ID/EX.RegisterRt
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRt
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRt

## Slide 263: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 20: Double Data Hazard & Forwarding

## Slide 264
Dependencies & Forwarding

## Slide 265
Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs = register number for Rs sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs, ID/EX.RegisterRt
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRt
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRt

## Slide 266
Detecting the Need to Forward
But only if forwarding instruction will write to a register!
E.g. sll $0, $1, 2
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not $zero
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0

## Slide 267
Forwarding Paths

## Slide 268
Forwarding Conditions
Mux control | Source | Explanation
ForwardA = 00 | ID/EX | The first ALU operand comes from the register file.
ForwardA = 10 | EX/MEM | The first ALU operand is forwarded from the prior ALU result.
ForwardA = 01 | MEM/WB | The first ALU operand is forwarded from data memory or an earlier ALU result.
ForwardB = 00 | ID/EX | The second ALU operand comes from the register file.
ForwardB = 10 | EX/MEM | The second ALU operand is forwarded from the prior ALU result.
ForwardB = 01 | MEM/WB | The second ALU operand is forwarded from data memory or an earlier ALU result.

## Slide 269
EX hazard: conditions & control signals

## Slide 270
MEM hazard: conditions & control signals

## Slide 271
Double Data Hazard
Consider the sequence:
  add $1,$1,$2 add $1,$1,$3 add $1,$1,$4
Both hazards occur
  Want to use the most recent
Revise MEM hazard condition
  Only fwd if EX hazard condition isn’t true

## Slide 272
Revised Forwarding Condition
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01

## Slide 273
Datapath with Forwarding

## Slide 274
Load-Use Data Hazard
Need to stall for one cycle

## Slide 275: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 21: Control Hazard

## Slide 276
Stalls and Performance
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure

## Slide 277
Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
In MIPS pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage

## Slide 278
When are branches resolved?
Instruction Fetch
Instruction Decode
Execute/
Address Calculation
Memory Access
Write Back
Branch target address is put in PC during Mem stage.

## Slide 279
Stall on Branch
Wait until branch outcome determined before fetching next instruction

## Slide 280
Stalling for Branch Hazards
beq $4, $0, there
and $12, $2, $5
or ...
add ...
sw ...
IM
Reg
DM
Reg
IM
Reg
IM
Reg
DM
IM
Reg
DM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Bubble
Bubble
Bubble

## Slide 281
Stalling for Branch Hazards
All branches waste 3 cycles.
  Seems wasteful, particularly when the branch isn’t taken.
It’s better to guess whether branch will be taken
  Easiest guess is “branch isn’t taken”

## Slide 282
Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In MIPS pipeline
  Can predict branches not taken
  Fetch instruction after branch, with no delay

## Slide 283
Assume Branch Not Taken
beq $4, $0, there
and $12, $2, $5
or ...
add ...
sw ...
IM
Reg
DM
Reg
IM
Reg
IM
Reg
DM
IM
Reg
DM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Works pretty well when you’re right – no wasted cycles

## Slide 284
Assume Branch Not Taken
beq $4, $0, there
and $12, $2, $5
or ...
add ...
there: sub $12, $4, $2
IM
Reg
IM
Reg
IM
IM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Flush
Flush
Flush
Same performance as stalling when you’re wrong
Whew! none of these
instruction have changed
memory or registers.

## Slide 285: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 22: Branch Hazard:I

## Slide 286
Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
In MIPS pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage

## Slide 287
When are branches resolved?
Instruction Fetch
Instruction Decode
Execute/
Address Calculation
Memory Access
Write Back
Branch target address is put in PC during Mem stage.

## Slide 288
Stall on Branch
Wait until branch outcome determined before fetching next instruction

## Slide 289
Stalling for Branch Hazards
beq $4, $0, there
and $12, $2, $5
or ...
add ...
sw ...
IM
Reg
DM
Reg
IM
Reg
IM
Reg
DM
IM
Reg
DM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Bubble
Bubble
Bubble

## Slide 290
Stalling for Branch Hazards
All branches waste 3 cycles.
  Seems wasteful, particularly when the branch isn’t taken.
It’s better to guess whether branch will be taken
  Easiest guess is “branch isn’t taken”

## Slide 291
Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In MIPS pipeline
  Can predict branches not taken
  Fetch instruction after branch, with no delay

## Slide 292
Assume Branch Not Taken
beq $4, $0, there
and $12, $2, $5
or ...
add ...
sw ...
IM
Reg
DM
Reg
IM
Reg
IM
Reg
DM
IM
Reg
DM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Works pretty well when you’re right – no wasted cycles

## Slide 293
Assume Branch Not Taken
beq $4, $0, there
and $12, $2, $5
or ...
add ...
there: sub $12, $4, $2
IM
Reg
IM
Reg
IM
IM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Flush
Flush
Flush
Same performance as stalling when you’re wrong
Whew! none of these
instruction have changed
memory or registers.

## Slide 294
MIPS with Predict Not Taken
Prediction correct
Prediction incorrect

## Slide 295
More-Realistic Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 296
Branch Hazards
If branch outcome determined in MEM
PC
Flush these instructions
(Set control values to 0)

## Slide 297
Branch Hazards- another e.g.
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
IM
Reg
ALU
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
beq $2, $1, here
here: lw ...
sub ...
lw ...
add ...
These instructions
shouldn’t be executed!
Finally, the right instruction

## Slide 298
Reducing Branch Delay
Move hardware to determine outcome to ID stage
  Target address adder
  Register comparator
Example: branch taken
  36: sub $10, $4, $8 40: beq $1, $3, 7 44: and $12, $2, $5 48: or $13, $2, $6 52: add $14, $4, $2 56: slt $15, $6, $7 ... 72: lw $4, 50($7)

## Slide 299
Example: Branch Taken

## Slide 300
Example: Branch Taken

## Slide 301
Reducing the Branch Delay
It’s easy to reduce stall to 2-cycles

## Slide 302
Reducing the Branch Delay
It’s easy to reduce stall to 2-cycles

## Slide 303
Stalling for Branch Hazards with branching in ID stage
beq $4, $0, there
and $12, $2, $5
or ...
add ...
sw ...
IM
Reg
DM
Reg
IM
Reg
IM
Reg
DM
IM
Reg
DM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Bubble

## Slide 304: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 23: Branch Hazard:II

## Slide 305
Eliminating the Branch Stall
There’s no rule that says we have to branch immediately. We could wait an extra instruction before branching.
The original SPARC and MIPS processors used a branch delay slot to eliminate single-cycle stalls after branches.
The instruction after a conditional branch is always executed in those machines, whether the branch is taken or not!

## Slide 306
Branch Delay Slot
beq $4, $0, there
and $12, $2, $5
there: xor ...
add ...
sw ...
IM
Reg
DM
Reg
IM
Reg
IM
Reg
DM
IM
Reg
DM
Reg
IM
Reg
DM
Reg
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
Branch delay slot instruction (next instruction after a branch) is executed even if the branch is taken.

## Slide 307
Scheduling the branch delay slot

## Slide 308
Filling the branch delay slot
The branch delay slot is only useful if you can find something to put there.
  Need earlier instruction that doesn’t affect the branch
If you can’t find anything, you must put a nop to insure correctness.
Worked well for early RISC machines.
  Doesn’t help recent processors much
  E.g. MIPS R10000, has a 5-cycle branch penalty, and executes 4 instructions per cycle.
Meanwhile, delayed branch is a permanent part of the ISA.

## Slide 309
Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction
  Branch prediction buffer (aka branch history table)
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 310
1-Bit Predictor: Shortcoming
Inner loop branches mispredicted twice!
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
  Mispredict as taken on last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around

## Slide 311
2-Bit Predictor
Only change prediction on two successive mispredictions

## Slide 312
Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 313: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 24-25: BTB & Exceptions

## Slide 314
Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 315
With all the branch prediction schemes discussed earlier, we still need to calculate the target address. This gives 1-cycle penalty for a taken branch.
If we need to reduce the branch penalty further, we need to fetch an instruction from the destination of a branch quickly. You need the next address at the same time as you’ve made the prediction.
This can be tough if you don’t know where that instruction is until the branch has been figured out. The solution is a table that remembers the resulting destination addresses of previous branches. This table is called the Branch Target Buffer (BTB) that caches the target addresses and is indexed by the complete PC value when the instruction is fetched.
Branch Target Buffer (BTB):

## Slide 316
That is, even before we have decoded the instruction and identified that it is a branch, we index into the BTB.
When the PC is used to fetch the next instruction, it is also used to index into the BTB. The BTB stores the PC value and the corresponding target addresses for some of the most recent taken branches.
If there is a hit and the instruction is a branch predicted taken, we can fetch the target immediately. This gives a zero cycle penalty for conditional branches. If there is no entry in the BTB, we follow the usual procedure and if it is a taken branch, make an entry in the BTB.
On the other hand, if the prediction is wrong, the penalty has to be paid and the BTB entry will have to be removed.
Branch Target Buffer (BTB):

## Slide 317
Let’s Think
Increasing the size of a branch prediction buffer means that it is less likely that two branches in a program will share the same predictor. A single predictor predicting a single branch instruction is generally more accurate than is that same predictor serving more than one branch instruction.
(a) List a sequence of branch taken and not taken actions to show a simple example of 1‐bit predictor sharing that reduces misprediction rate.
Consider two branches, B1 and B2, that are executed alternately. During the execution of the program, B1 and B2 each alternate taken/not taken. If they each had a 1‐bit predictor, each would always be mispredicted.

## Slide 318
In the table below, columns labelled P show the value of a 1‐bit predictor shared by B1 and B2. Columns labelled B1 and B2 show the actions of the branches (each alternating taken/not taken). Time increases to the right. T stands for taken, NT for not taken. The predictor is initialized to NT.
Because a single predictor is shared, prediction accuracy improves from 0% to 50%.
Contd..

## Slide 319
b) List a sequence of branch taken and not taken actions that show a simple example of how sharing a 1‐bit predictor increases misprediction. Here, B1 is always taken, B2 is always not taken, and they are interleaved as in (a)
If each had a 1‐bit predictor, each would be correctly predicted after the initial startup transient. Because a single predictor is shared, accuracy is 0%
Contd..

## Slide 320
This exercise examines the accuracy of various branch predictors for the following repeating patterns (e.g., in a loop) of branch outcomes. Accuracy is defined as the percentage of guesses that are correct.
3.1 (a) T, NT, NT, NT, T
3.1.1 What is the accuracy of always-taken and always-not-taken predictors for this sequence of branch outcomes?
Measuring branch predictor accuracy

## Slide 321
Always-Taken Predictor ‘
Actual T NT NT NT T
Predict T T T T T
Accuracy = 2/5 = 0.4
Always-not-taken Predictor
Actual T NT NT NT T
Predict NT NT NT NT NT
Accuracy = 3/5 = 0.6
Contd..

## Slide 322
What is the accuracy of a predict-last-taken predictor for the first 5 branches in this sequence? Assume this predictor starts in the ”Predict not taken” state.
Actual T NT NT NT T
Predict NT T NT NT NT
Accuracy = 2/5 = 0.4
Contd..

## Slide 323
What is the accuracy of a 2-bit predictor for the first 5 branches in this sequence? Assume this predictor starts in the ”Strongly not taken” state.
Actual T NT NT NT T
Solution?
What is the accuracy of a 2-bit predictor if this pattern is repeated forever?
Actual T NT NT NT T | T NT NT NT T | T NT NT NT T |
Solution?
Contd..

## Slide 324
What is the accuracy of a predict-last-taken predictor for the first 5 branches in this sequence? Assume this predictor starts in the ”Predict not taken” state
Actual T NT T NT T
Predict NT T NT T NT
Accuracy = 0/5 = 0
Contd..

## Slide 325
Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU
    e.g., undefined opcode, overflow, syscall, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard

## Slide 326
Handling Exceptions
In MIPS, exceptions managed by a System Control Coprocessor (CP0)
Save PC of offending (or interrupted) instruction
  In MIPS: Exception Program Counter (EPC)
Save indication of the problem
  In MIPS: Cause register
  We’ll assume 1-bit
    0 for undefined opcode, 1 for overflow
Jump to handler at 8000 00180

## Slide 327
An Alternate Mechanism
Vectored Interrupts
  Handler address determined by the cause
Example:
  Undefined opcode: C000 0000
  Overflow: C000 0020
  …: C000 0040
Instructions either
  Deal with the interrupt, or
  Jump to real handler

## Slide 328
Handler Actions
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  use EPC to return to program
Otherwise
  Terminate program
  Report error using EPC, cause, …

## Slide 329
Exceptions in a Pipeline
Another form of control hazard
Consider overflow on add in EX stage
  add $1, $2, $1
  Prevent $1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Set Cause and EPC register values
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware

## Slide 330
Exception Properties
Restartable exceptions
  Pipeline can flush the instruction
  Handler executes, then returns to the instruction
    Refetched and executed from scratch
PC saved in EPC register
  Identifies causing instruction
  Actually PC + 4 is saved
    Handler must adjust

## Slide 331
Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once
Simple approach: deal with exception from earliest instruction
  Flush subsequent instructions
  “Precise” exceptions
In complex pipelines
  Multiple instructions issued per cycle
  Out-of-order completion
  Maintaining precise exceptions is difficult!

## Slide 332
Imprecise Exceptions
Just stop pipeline and save state
  Including exception cause(s)
Let the handler work out
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion
Simplifies hardware, but more complex handler software
Not feasible for complex multiple-issue out-of-order pipelines

## Slide 333
Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
    CPI < 1, so use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue
    But dependencies reduce this in practice

## Slide 334
Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 335
Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated

## Slide 336
Compiler/Hardware Speculation
Compiler can reorder instructions
  e.g., move load before branch
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed
  Flush buffers on incorrect speculation

## Slide 337
Speculation and Exceptions
What if exception occurs on a speculatively executed instruction?
  e.g., speculative load before null-pointer check
Static speculation
  Can add ISA support for deferring exceptions
Dynamic speculation
  Can buffer exceptions until instruction completion (which may not occur)

## Slide 338
Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)

## Slide 339: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 26: ILP

## Slide 340
Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary

## Slide 341
MIPS with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 342
MIPS with Static Dual Issue

## Slide 343
Hazards in the Dual-Issue MIPS
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add $t0, $s0, $s1 load $s2, 0($t0)
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required

## Slide 344
Scheduling Example
Schedule this for dual-issue MIPS
Loop: lw $t0, 0($s1) # $t0=array element addu $t0, $t0, $s2 # add scalar in $s2 sw $t0, 0($s1) # store result addi $s1, $s1,–4 # decrement pointer bne $s1, $zero, Loop # branch $s1!=0
 | ALU/branch | Load/store | cycle
Loop: | nop | lw $t0, 0($s1) | 1
 | addi $s1, $s1,–4 | nop | 2
 | addu $t0, $t0, $s2 | nop | 3
 | bne $s1, $zero, Loop | sw $t0, 4($s1) | 4
  IPC = 5/4 = 1.25 (c.f. peak IPC = 2)

## Slide 345
Loop Unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Called “register renaming”
  Avoid loop-carried “anti-dependencies”
    Store followed by a load of the same register
    Aka “name dependence”
      Reuse of a register name

## Slide 346
Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at cost of registers and code size
 | ALU/branch | Load/store | cycle
Loop: | addi $s1, $s1,–16 | lw $t0, 0($s1) | 1
 | nop | lw $t1, 12($s1) | 2
 | addu $t0, $t0, $s2 | lw $t2, 8($s1) | 3
 | addu $t1, $t1, $s2 | lw $t3, 4($s1) | 4
 | addu $t2, $t2, $s2 | sw $t0, 16($s1) | 5
 | addu $t3, $t4, $s2 | sw $t1, 12($s1) | 6
 | nop | sw $t2, 8($s1) | 7
 | bne $s1, $zero, Loop | sw $t3, 4($s1) | 8

## Slide 347
Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 348
Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s4, $s4, $t3 slti $t5, $s4, 20
  Can start sub while addu is waiting for lw

## Slide 349
Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 350
Speculation
Predict branch and continue issuing
  Don’t commit until branch outcome determined
Load speculation
  Avoid load and cache miss delay
    Predict the effective address
    Predict loaded value
    Bypass stored values to load unit
  Don’t commit load until speculation cleared

## Slide 351
Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 352
Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well

## Slide 353: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 27,28: Memory

## Slide 354
Large and Fast: Exploiting Memory Hierarchy
Chapter 5

## Slide 355
Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data

## Slide 356
Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU

## Slide 357
Memory Hierarchy Levels
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio

## Slide 358
Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $500 – $1000 per GB
Dynamic RAM (DRAM)
  50ns – 70ns, $3 – $6 per GB
Magnetic disk
  5ms – 20ms, $0.01 – $0.02 per GB
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk

## Slide 359
DRAM Technology
Data stored as a charge in a capacitor
  Single transistor used to access the charge
  Must periodically be refreshed
    Read contents and write back

## Slide 360
DRAM Generations
Year | Capacity | $/GB
1980 | 64 Kibibit | $6,480,000
1983 | 256 Kibibit | $1,980,000
1985 | 1 Mebibit | $720,000
1989 | 4 Mebibit | $128,000
1992 | 16 Mebibit | $30,000
1996 | 64 Mebibit | $9,000
1998 | 128 Mebibit | $900
2000 | 256 Mebibit | $840
2004 | 512 Mebibit | $150
2007 | 1 Gibibit | $40
2010 | 2 Gibibit | $13
2012 | 4 Gibibit | $5
2015 | 8 Gibibit | $7
2018 | 16 Gibibit | $6

## Slide 361
Flash Storage
Nonvolatile semiconductor storage
  100× – 1000× faster than disk
  Smaller, lower power, more robust
  But more $/GB (between disk and DRAM)

## Slide 362
Disk Storage
Nonvolatile, rotating magnetic storage

## Slide 363
Disk Sectors and Access
Each sector records
  Sector ID
  Data (512 bytes, 4096 bytes proposed)
  Error correcting code (ECC)
    Used to hide defects and recording errors
  Synchronization fields and gaps
Access to a sector involves
  Queuing delay if other accesses are pending
  Seek: move the heads
  Rotational latency
  Data transfer
  Controller overhead

## Slide 364
Disk Access Example
Given
  512B sector, 15,000rpm, 4ms average seek time, 100MB/s transfer rate, 0.2ms controller overhead, idle disk
Average read time
  4ms seek time + ½ / (15,000/60) = 2ms rotational latency + 512 / 100MB/s = 0.005ms transfer time + 0.2ms controller delay = 6.2ms
If actual average seek time is 1ms
  Average read time = 3.2ms

## Slide 365
Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
How do we know if the data is present?
Where do we look?

## Slide 366
Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits

## Slide 367
Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 368
Cache Example
8-blocks, 1 word/block, direct mapped
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 369
Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 370
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010
Cache Example

## Slide 371
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010
Cache Example

## Slide 372
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000
Cache Example

## Slide 373
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010
Cache Example

## Slide 374
Address Subdivision

## Slide 375: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 29-31: Cache, Virtual Memory

## Slide 376
Address Subdivision

## Slide 377
Example: Larger Block Size
64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address = 1200/16 = 75
Block number = 75 modulo 64 = 11
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits

## Slide 378
Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
  Larger blocks  pollution
Larger miss penalty
  Can override benefit of reduced miss rate
  Early restart and critical-word-first can help

## Slide 379
Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 380
Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 381
Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 382
Write Allocation
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: fetch the block
  Write around: don’t fetch the block
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually fetch the block

## Slide 383
Main Memory Supporting Caches
Use DRAMs for main memory
  Fixed width (e.g., 1 word)
  Connected by fixed-width clocked bus
    Bus clock is typically slower than CPU clock
Example cache block read
  1 bus cycle for address transfer
  15 bus cycles per DRAM access
  1 bus cycle per data transfer
For 4-word block, 1-word-wide DRAM
  Miss penalty = 1 + 4×15 + 4×1 = 65 bus cycles
  Bandwidth = 16 bytes / 65 cycles = 0.25 B/cycle

## Slide 384
Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
With simplifying assumptions:

## Slide 385
Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
Miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster

## Slide 386
Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 387
Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)

## Slide 388
Associative Cache Example

## Slide 389
Spectrum of Associativity
For a cache with 8 entries

## Slide 390
Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 

## Slide 391
Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 

## Slide 392
How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 393
Set Associative Cache Organization

## Slide 394
Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 395
Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 396
Multilevel Cache Example
Given
  CPU base CPI = 1, clock rate = 4GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 397
Example (cont.)
Now add L-2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  Penalty = 5ns/0.25ns = 20 cycles
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6

## Slide 398
Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single cache
  L-1 block size smaller than L-2 block size

## Slide 399
Virtual Machines
Host computer emulates guest operating system and machine resources
  Improved isolation of multiple guests
  Avoids security and reliability problems
  Aids sharing of resources
Virtualization has some performance impact
  Feasible with modern high-performance comptuers
Examples
  IBM VM/370 (1970s technology!)
  VMWare
  Microsoft Virtual PC

## Slide 400
Virtual Memory
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)
Programs share main memory
  Each gets a private virtual address space holding its frequently used code and data
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a page
  VM translation “miss” is called a page fault

## Slide 401
Address Translation
Fixed-size pages (e.g., 4K)

## Slide 402
Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS code
Try to minimize page fault rate
  Fully associative placement
  Smart replacement algorithms

## Slide 403
Page Tables
Stores placement information
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  PTE stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk

## Slide 404
Translation Using a Page Table

## Slide 405
Mapping Pages to Storage

## Slide 406
Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written

## Slide 407
Fast Translation Using a TLB
Address translation would appear to require extra memory references
  One to access the PTE
  Then the actual memory access
But access to page tables has good locality
  So use a fast cache of PTEs within the CPU
  Called a Translation Look-aside Buffer (TLB)
  Typical: 16–512 PTEs, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate
  Misses could be handled by hardware or software

## Slide 408
Fast Translation Using a TLB

## Slide 409
TLB Misses
If page is in memory
  Load the PTE from memory and retry
  Could be handled in hardware
    Can get complex for more complicated page table structures
  Or in software
    Raise a special exception, with optimized handler
If page is not in memory (page fault)
  OS handles fetching the page and updating the page table
  Then restart the faulting instruction

## Slide 410
TLB Miss Handler
TLB miss indicates
  Page present, but PTE not in TLB
  Page not preset
Must recognize TLB miss before destination register overwritten
  Raise exception
Handler copies PTE from memory to TLB
  Then restarts instruction
  If page not present, page fault will occur

## Slide 411
TLB and Cache Interaction
If cache tag uses physical address
  Need to translate before cache lookup
Alternative: use virtual address tag
  Complications due to aliasing
    Different virtual addresses for shared physical address

## Slide 412: CS F342: Computer Architecture
Dr. Nikumani Choudhury
Asst. Prof., Dept. of Computer Sc. & Information Systems
nikumani@hyderabad.bits-pilani.ac.in
(First Semester 2022-23)
Lect 32-33: Cache, Virtual Memory

## Slide 413
Cache Design Trade-offs
Design change | Effect on miss rate | Negative performance effect
Increase cache size | Decrease capacity misses | May increase access time
Increase associativity | Decrease conflict misses | May increase access time
Increase block size | Decrease compulsory misses | Increases miss penalty. For very large block size, may increase miss rate due to pollution.

## Slide 414
Cache Coherence Problem
Suppose two CPU cores share a physical address space
  Write-through caches
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
2 | CPU B reads X | 0 | 0 | 0
3 | CPU A writes 1 to X | 1 | 0 | 1

## Slide 415
Coherence Defined
Informally: Reads return most recently written value
Formally:
  P writes X; P reads X (no intervening writes)  read returns written value
  P1 writes X; P2 reads X (sufficiently later)  read returns written value
    c.f. CPU B reading X after step 3 in example
  P1 writes X, P2 writes X  all processors see writes in the same order
    End up with the same final value for X

## Slide 416
Cache Coherence Protocols
Operations performed by caches in multiprocessors to ensure coherence
  Migration of data to local caches
    Reduces bandwidth for shared memory, and latency
  Replication of read-shared data
    Reduces contention for access, latency
Snooping protocols
  Each cache monitors bus reads/writes

## Slide 417
Typical collection of storage and I/O devices
Because we use storage systems to preserve our data for us, it is of the utmost importance that we can depend upon them to do so.

## Slide 418
The standard for dependability is higher for storage systems than it is for computation.
It is one thing for a processor to hang or even crash, but another if a hard disk fails.
A processor crash is usually just an inconvenience but a disk failure might mean irreplaceable data loss.
Therefore, storage systems place greater emphasis on:
Dependability
Cost
Expandability
Storage Systems

## Slide 419
Dependability is the quality of a system such that reliance can be placed on its service. The service delivered by a system is its observed actual behavior as perceived by another system that interacts with it. The other system may be a machine, a person, or both.
Reliability is a measure of continuous service accomplishment. Equivalently, it can be measured by the mean time to failure (MTTF). (The amount of time it is available without interruption, on average.)
The number of failures that can be expected in a single year – and it is called the annual failure rate, or AFR.
Example. If a disk drive has a 1,500,000 MTTF, then, recalling that there are 8760 hours in a year, its AFR is 8760/1500000= .00584. If a company owns 100,000 such disk drives, then we would expect 0.00584*100000=584 disk failures each year, which is more than one disk failing every day.
Dependability, Reliability, and Availability

## Slide 420
Service interruption is measured by how long a system is unavailable, which is characterized by the mean time to repair (MTTR). Mean time to repair is the average amount of time that it takes for a device to be restored to the available state from the unavailable state.
The MTTF alone does not characterize the availability of a device, because if the interval from the moment of failure to the moment at which it is restored is long, the fraction of available time is diminished.
A more comprehensive characterization is the sum of the MTTF and the MTTR and is called the mean time between failures (MTBF).
Availability is defined as,
Availability = MTTF/ (MTTF + MTTR) = MTTF/MTBF
Availability

## Slide 421
Example
A system's performance is observed over the course of 185 days and the following data was recorded:
after which it stayed up. Assuming that the events occurred at the ends of the given days, the MTTF is
(10 + (92-12) + (140-95 + (180-145) ) /4 = (10+80+45+35)/4 = 42.5
The MTTR is (2+3+5+5)/4 = 3.75
Availability is 42.5/(42.5+3.75) = 0.92.

## Slide 422
Should performance be measured by
• system throughput (jobs completed per unit time), or
• response time?
Throughput can be measured by bandwidth, either
number of completed I/O operations per unit time, or
number of bytes transferred per unit time
Assessing Performance

## Slide 423
Examples.
Transaction processing systems such as on-line commerce applications and on-line banking systems have to handle a large number of small transactions, so (1) is a better measure than (2).
A system for delivering streaming video, on the other hand, is better measured by the volume of bytes transferred per unit time (2) than by the number of completed transactions.
Throughput is not always the best measure. Sometimes response time is more important. Often not just the mean response time, but the standard deviation of response times (indicates how reliable the system is). For single-user workstations, response time is typically the most important performance measure.
Sometimes both are equally important:
3. ATM networks, file servers, and web servers must have short response times for their customers and must also process large amounts of data quickly.
Assessing Performance

## Slide 424
Memory Storage Systems

## Slide 425
Types of Access
RANDOM ACCESS (Main Memory, Flash)
  items are independently addressed
  access time is constant
DIRECT ACCESS (Disc Drives)
  items are independently addressed in regions
  access time is variable—though not significantly
SEQUENTIAL ACCESS (Tape Systems)
  items are organized in sequence (linearly)
  access time is significantly variable

## Slide 426
Tape Drives in action…1950’s-70’s

## Slide 427
Disk Drives circa 1980
66Mb 400 lbs! $40,000 each

## Slide 428
Floppy / Hard Disks (Magnetic)
Direct Access Devices

## Slide 429
Micro Drive
Disk capable of storing 64 GIGABYTES

## Slide 430
Direct Access
SEEK — controller advances read/write head to proper track
LATENCY — waits for proper sector to rotate under head
READ/WRITE — disk head scans the sector for read or write

## Slide 431
Disk Technology
  Disk access time = seek time + rotational delay + transfer time

## Slide 432
Optical Disk
Compact Disc–Read Only Memory (CD-ROM)
  archived and published information
  Relatively high capacity (650 Mbytes)
Compact Disc–Recordable (CD-RW
  recordable
  readable using CD-ROM technology
Digital Versatile Discs (DVD)/DVD-R)
  Very high capacity, storages (5-15 Gbytes)
  Multiple Layers, tighter spacing in the same size as CD
  And then…
  BLUE RAY (3-10 times the capacity of today’s DVDs)

## Slide 433
Optical Drive Reading and Writing
discs are “burnt” one at a time
high intensity red
or blue laser beam used for reading/ recording pregrooved tracks
low intensity beam for reading/ higher intensity for burning

## Slide 434
Flash Memory
Non Volatile Memory
Small, Convenient and Reliable
Random Access
Relatively expensive in terms of cost/Mb compared to Dynamic RAM
Not as fast as Dynamic Ram
Prices dropping every day, capacity increasing!

## Slide 435
I/O System
The I/O subsystem is treated as an independent unit in the computer
  The CPU initiates I/O commands generically
    Read, write, scan, etc
    This simplifies the CPU
  I/O modules are components that connect an I/O device to the I/O bus
    The I/O module is an intermediary between CPU and the I/O device, and possibly between memory and the I/O device
  This allows us to tailor I/O devices to specific uses without having to worry about how the CPU might be able to handle that new type of device
  In addition, while the CPU may initiate an I/O operation, once begun, the I/O module takes over so that the CPU can get back to doing whatever it was doing
    There are 4 general forms of I/O control, we will cover each

## Slide 436
I/O Architectures
I/O subsystem will typically include
  Blocks of memory dedicated to I/O buffering
  I/O bus(es)
  I/O devices
  Specialized interfaces (for instance for keyboard and monitor) and interface cards
  Possibly other connections (network, cable, etc)

## Slide 437
RAID
Hard disk storage is critically important because of our reliance on the hard disk to store virtually everything
  However, the hard disk is the most likely component to fail on us because of its usage and its high speed
  If we want reliable access, we might want to use a degree of redundancy by adding additional disks to our drive unit
    This is the idea behind RAID
      Redundant array of independent disks (or)
      Redundant array of inexpensive disks
  There are 7 forms (or levels) of RAID, each one different, and each with its own strengths and weaknesses

## Slide 438
RAID
RAID 0 offers no redundancy, but improves disk access
Here, files are broken into strips and distributed across disk surfaces (known as disk spanning) so that access to a single file can be done in parallel disk accesses
RAID 1 creates a mirror for every disk giving
100% redundancy at twice the cost, 2 reads
can be done in parallel, one from each mirror,
but writes require saving to both sets of disk

## Slide 439
RAID
RAID 1 may be too expensive, so an alternative is to just store parity information
RAID 2 strips each byte into 1 bit per disk and uses additional disks to store Hamming codes for redundancy
Hamming code information is time consuming to generate, so RAID 2 is not used, instead RAID 3 uses the same idea but only retains parity information for redundancy
RAID 3 is most suitable for small computer systems that require some but not total redundancy

## Slide 440
RAID
In RAID 4, all parity information is placed on a single disk which creates a bottleneck and so defeats the advantage of parallel accesses (if I/O requests require accessing a strip plus
the parity disk, then only 1 access can occur at a time)
In RAID 5, parity information is interleaved across disks so that
hopefully two accesses can take place in parallel
In RAID 6, parity information is duplicated for greater redundancy